## Slide 1: Lab C : Corner Tracking with Optical Flow
柯宗賢, 黃意堯, 劉彥甫
INSTRUCTOR: Professor Jiin Lai

## Slide 2: Outline
Background Introduction
  What is an optical flow?
  How do we estimate optical flow?
Pipeline Applications : Corner Tracking with Harris corner detector
  Main function of the OpenCL host function
  Kernel functions
Performance Analysis
The result of cornertracker
Suggestion for Improvement

## Slide 3: What is an Optical Flow?
Optical flow is a pattern of apparent motion of objects, edges in a visual scene caused by the relative motion between an observer and a scene.
Optical flow can be used by roboticist, encompassing related techniques from imaging processing and control of navigation including motion detection, object segmentation, motion compensated ending, and stereo disparity measurement.

## Slide 4: How do we Estimate Optical Flow
For a 2D+t dimensional cases a voxel, volume pixel, at location (x, y, t) with intensity I(x, y, t) will have moved by x, y, and t between the two image frames, and the following brightness constantly constraint can be giver:
I(x, y, t) = I(x + x, y + y, t + t)
Assuming the movement to be very small between contiguous frames, the image constraint at I(x, y, t) with Taylor series can be developed to get:
I(x + x, y + y, t + t) = I(x, y, t)
Then we can get this term with higher order truncated:
Dividing by t:

## Slide 5: Corner Tracking with Harris Corner Detector
The structure of OpenCL host function is:
1) Read Video
2) Corner tracking for each frame
  Detect harris corner
  Computer dense optical flow for current frame and next frame
  Update locations of corners

## Slide 6: Main Function of the OpenCL Host Function
host function:
Corner Tracking Accelerator:
In the corner tracking function, we use dataflow to accelerate the pipeline of three kernel functions: Array2xfMat, cornerHarris and cornersImgToList.

## Slide 7: Main Function of the OpenCL Host Function
Pyramid Dense Optical Flow Accelerator:
Corner Update Accelerator:
In the pyramid dense optical flow function, we use dataflow to accelerate the pipeline of three kernel functions: Array2xfMat, densePyrOpticalFlow and xfMat2Array.

## Slide 8: Kernel Functions
Array2xfMat
CornerHarris
CornersImgToList
Dense Optical Flow Computation

## Slide 9: Array2xfMat
There are two type of NPC, number of pixels to be processed per cycle.
Possible option are XF_NPPC1 and XF_NPPC8 for 1-pixel and 8-pixel operations respectively.
In our Lab C, we use XF_NPPC1 for our NPC.
The first thing here is to transfer Array into xfMat format with above function.

## Slide 10: CornerHarris
After perform sobel filter, we can get gradient of x and y direction.
In sobel filter, it already use #pragma array partition complete dim=1. It is very similar to FIR computation if we flatten the sobel filter operation.
After getting gradients, we first duplicate them with xFDuplicate.
And we perform gradient_x * gradient_y with xFMultiply.
And then perform three mean filter, box filter, on the gradient_x/y square and gradient_x*y.

## Slide 11: CornerHarris
Array partition in Sobel filter:

## Slide 12: CornerHarris
With these three array, we now have M matrix as following.
After we have M matrix, we can calculate “Harris response” with following formula

## Slide 13: CornerHarris
And K in the xFComputeScore is an empirical constant which is usually range form 0.04 to 0.06. After score computation, we need to do a max suppression. Before max suppression, we first perform an activation function with threshold.
Last task is Max suppression.
Basically what the CornerHarris does is to reduce maxima into only one local maxima point.
This will makes us to find a corner which can represent this area. And we need to add those corner coordinates into a list.

## Slide 14: CornersImgToList
tempValue is 255 if there is a corner

## Slide 15: Dense Optical Flow Computation
Compute feature map with convolution on cur_frame and nxt_frame with 5x5 Gaussian filter as following figure.

## Slide 16: Dense Optical Flow Computation
First, we split the u and v vector from stream data using split_stream_int_fixed.
And we can perform scale up if vector is scale down before by scale_up.

## Slide 17: Dense Optical Flow Computation
And first thing we should find the intensity by findIntensity.
After we find the intensity, we can then substrate it from the equation below by findGradients.

## Slide 18: Dense Optical Flow Computation
The next step is to compute hessian matrix by find_G_and_b_matrix.
After computing u,v, we apply a median filter on both vectors.
Then stitched the u,v vector into same data array and stream it out.
On the top function, we perform following iterated algorithm until it converge.
Now we can perform corner coordinates update. In this case, we can track the corner.

## Slide 19: Performance Analysis
cornerTracker
pyr_down_accel
pyr_dense_optical_flow_accel
cornerupdate_accel

## Slide 20: CornerTracker
clEnqueueMigrateMemObjects
clCreateBuffer
clSetKernelArg
clWaitForEvents
clEnqueueTask
In the cornertracker, the code is following the flow:
cl::Buffer
q.enqueueMigrateMemObjects
krnl.setArg
q.enqueueTask
clWaitForEvents
q.enqueueMigrateMemObjects
We can see that the flow is the same as the application timeline.

## Slide 21: Pyr_down_accel
In pyr_down_accel, the timeline is similar to cornerTracker. The only different is clFinish in pyr_down_accel which is add behind q.enqueueMigrateMemObjects.

## Slide 22: Pyr_dense_optical_flow_accel
clWaitForEvents
clSetKernelArg
clEnqueueTask
In a pyr_dense_optical_flow_accel, there have 16 of _krnl.setArg in application timeline which is the same as we defined in the code.

## Slide 23: Pyr_dense_optical_flow_accel
In a complete pyr_dense_optical_flow_accel, we can see that it used a q.enqueueMigrateMemObjects before five kernel of pyr_dense_optical_flow_accel.

## Slide 24: Cornerupdate_accel
clEnqueueMigrateMemObjects
clCreateBuffer
clSetKernelArg
clWaitForEvents
clEnqueueTask
clFinish

## Slide 25: The Whole Application Timeline in Vitis HW
Run through four kernels
Lab C in vitis hardware, first we should read the data from binary_file. Then we can begin to corner tracking. Then we do four times corner tracking, so we can see four parts in the application timeline.

## Slide 26: The Result of Cornertracker
In the lab, first we will build a pyramid of input photo. And then go through the whole system, we can get the result.

## Slide 27: The Result of Cornertracker
We can see the result have some mark which is the corner which we find by the code.

## Slide 28: Suggestion for Improvement
For the current implementation:
However, detect Harris corners can be executed parallel with compute dense optical flow to accelerate the applications. This optimization can be done in OpenCL host code.

## Slide 29: GitHub
The GitHub link : https://github.com/Waxpple/HLS_2021_FALL_LABC

## Slide 30
Thanks for listening！