## Slide 1: Lab C Vitis library
Group 3: 黃友杉, 王皓仁, 張鶴騰

## Slide 2: About vision library
Vision library functions
  https://xilinx.github.io/Vitis_Libraries/vision/2020.2/index.html
Vision library examples
  https://xilinx.github.io/Vitis_Libraries/vision/2020.2/overview.html
Open CV functions can almost find their counterparts in Vision
  in namespace xf::cv
  i.e., hardware accelerated Open CV
Open CV is often used in NN training framework
  Darknet etc.

## Slide 3: Overview
Get familiar with Vision library
  NN applications
Goal: implement a function augmenting training images
  Images are slightly modified in NN training process
  Increase model robustness -> reduce overfitting
Components:
  Vitis vision L3 “blobfromimage”
  Migrates functions from 2021 to 2020.2
  Implement corresponding functions in testbench

## Slide 4: Utilities
resize
crop
flip
Ex: xfMat2Array<OUTPUT_PTR_WIDTH, OUT_TYPE, MAX_HEIGHT, MAX_ WIDTH, NPC>( … )
Arguments | Functionality | Example
OUTPUT_PTR_WIDTH | The unit width of output ap type data | ap_uint<OUTPUT_PTR_WIDTH>
OUT_TYPE | Width of output bit and channel | XF_8UC3
MAX_HEIGHT | Max height of an image | 
MAX_ WIDTH | Max width of an image | 
NPC | Pixels processed per cycle | XF_NPPC1

## Slide 5: xf::cv::preProcessing
Op code | Operation | Description
0 |  | Mean subtraction
1 |  | Scale and clip
2 |  | Clipping
3 |  | Scale and bias
4 |  | Scale and bias with Mean subtraction
5 |  | Full operation
Op code | Operation | Description
0 |  | Mean subtraction
1 |  | Scale and clip
2 |  | Clipping
3 |  | Scale and bias
4 |  | Scale and bias with Mean subtraction
5 |  | Full operation

## Slide 6: Observations
Synthesis report:
  Estimated clock period: 3.271 ns.
  Latency: min: 0.304 ms, max: 7.025 ms.
  Utilization:
Software latency v.s. hardware latency:
  Software: 50.849 ms.
  Hardware: 1.92512 ms.
  26x speed up by using FPGA accelerators
W/WO stream
  Only differs in 9 FFs usage.
  Other metrices are the same, such as delay
W/WO dataflow:
  kernel seems to halt mysteriously when dataflow is deactivated
BRAM | DSP | FF | LUT
100 | 20 | 19611 | 34058

## Slide 7: Suggestions for improvement
Option 1: improve current kernel’s internal streaming
  Some of invoked functions might not support stream
Option 2: host level parallelism
  Instead of invest more resource improving a kernel
  We may instantiate multiple kernel instances
  Dispatch jobs parallelly
  Similar to multi-threading. But now a thread corresponds to a kernel instance

## Slide 8: Supplement
Compatibility issues between Vitis and system libraries:
  Problem: v++ 2020.2 does not provide up-to-date stdc++ library required by third-party packages
  Solution: it’s safe to replace the libstdc++ used by v++ with a newer version
Basic functions in 2021 may be absent in 2020.2
  e.g., xf::cv::flip
  Check compiler’s error message
  It’s safe to manually update infrastructure defined in “L1/include/”