## Slide 1: Lab C: Vitis Vision Library
Homography Warpping
Team 4
Date: 2021/11/29
https://github.com/Yuoto/labC

## Slide 2: Overview
Homography and Warping
Kernel Code
Kernel Optimization
Benchmark
Application Demo
Appendix

## Slide 3: Warping
Per-pixel transforming problem
Transform by matrix multiplication

## Slide 4: Homography(1/2)
Mapping between planes
Planar pose estimations

## Slide 5: Homography(2/2)
Per-pixel matrix multiplication problem

## Slide 6: Kernel Code

## Slide 7: Kernel Code － Data Type
Pixel Type
Pixel-Level Parallelism
 | Option | #bits per Pixel | #Channels
Gray | XF_8UC1 | 8 | 1
RGB | XF_8UC3 | 8 | 3
Option | Description
XF_NPPC1 | Process 1 pixel per clock cycle
XF_NPPC2 | Process 2 pixels per clock cycle
XF_NPPC4 | Process 4 pixels per clock cycle
XF_NPPC8 | Process 8 pixels per clock cycle

## Slide 8: Kernel Code － I/O Stream
DATAFLOW
XF_BITSHIFT(NPC): Pixel-Level Parallelism

## Slide 9: Kernel Code － Buffer (1/2)
4 memory blocks
  Bilinear Interpolation
  Assign each pixel to one memory according to the parity of its column and row

## Slide 10: Kernel Code － Buffer (2/2)
4 memory blocks
  1 block size: STORE_ROWS/4 x image width
  Write one pixel per cycle
  Start to overwrite the buffer if the index of executed row > STORE_ROWS
  If the pixel is not in the buffer, write 0 to output stream instead.

## Slide 11: Kernel Code － Backward Warp
2-level nested loop
  Loop bound:
    1st (img_rows + START_ROW)
    2nd image width
  Steps
Store input image to buffer
Compute which pixel of input image should be outputted after START_ROW
Bilinear Interpolation
Retrieve that pixel from buffer

## Slide 12: todo: Kernel Optimization
Although there exists SIMD-like parallelism
Loop bound of the main loop is fixed to UHD
  UHD 3840*2160

## Slide 13: Benchmark: 4K UHD Gray/ RGB
Single Shot
Workstation CPU
auto start = std::chrono::high_resolution_clock::now();
std::chrono::duration_cast<std::chrono::milliseconds>(std::chrono::high_resolution_clock::now() - start).count()
 | 4K Gray | 4K RGB
CPU | 373 ms | 
FPGA kernel | 29.16 ms | 
FPGA data transfer | 9.14/0.86 ms | 

## Slide 14: Application Acceleration
Marker Detection
Homography Estimation
Inverse warp
Template

## Slide 15: Appendix: Add Library in GUI
Similar as Visual Studio
Compile from source or pre-compiled binary
Add include file, library path, symbol to project properties
Eigen, Boost, OpenGL, … etc

## Slide 18: Summary
Application acceleration design in Vitis
Design memory array storage for certain algorithm
Library import in GUI mode

## Slide 19: TODO
Add benchmark to 4K UHD RGB video stream input
Optimize the main loop